## Slide 1: Device –High performance
SOC needs additional capabilities such as an external application-speciﬁc I/O device. The device interface consists of a device interface controller and a deﬁned external interconnect to attach to an external device.
A peripheral bus interface requires a number of capabilities:
1. Transaction mapping from the processor to the device address space :
Captures transactions directed to the memory address of the external bus and associated device, and translates the transaction (read or write) into the appropriate transaction on the expansion bus.

## Slide 2
Inbound transactions—For high-performances interfaces, it is important that the expansion interface allow the external devices to read and write resources in the SOC. This is often called bus mastering.
Interrupts—Interactions with a high-performance device require the ability to route interrupts from the device to the processor.
Physical standard—Some interface deﬁnitions also include a physical connector standard, such as card size. A physical standard allows the system to be expanded with many different capabilities. The Peripheral Component Interconnect (PCI) is an excellent example of this

## Slide 3: PCIe
PCI Express (PCIe) is the third generation of the PCI standard.
higher-performance I/O bus used to connect peripheral devices to compute systems.
PCIe is used on Intel architecture systems, but it has become popular on many platforms.
The PCIe standard is developed by the PCI-SIG

## Slide 4: Features Of Pci-Bus Enumeration
Capability to identify devices attached to a PCIe bus at runtime. Once these devices are discovered, the system software can allocate resources to these devices dynamically
Allocates a range of addresses in the system address map to access the device.
as well as one or more interrupt vectors
The process of enumeration is a runtime search through the PCI conﬁguration space looking for devices

## Slide 5: Configuration space
a special PCIe bus space to facilitate the enumeration process.
space size is a total of 256 MB.
supports device discovery and initial conﬁguration by responding to special conﬁguration space transactions on the bus.
Partitioned into PCIe busses (up to 256), devices per bus (up to 32), and functions within a device (up to 8 per device). This three tuple address is known as the Bus Device Function (BDF) address.

## Slide 6: BDF
The BDF address for a device depends on where it is connected to on the PCIe fabric.
The function is dedicated by the design of the device. For example, if a Ethernet card has two separate Ethernet interfaces, it will mostly likely present two separate functions.

## Slide 7: PCIe hierarchy
The head of the PCIe hierarchy is known as the root complex
takes processor read/write transactions and routes them to the appropriate transaction type in the PCIe fabric.
It also routes interrupts from the devices to the appropriate processor.
Devices can also be integrated into the root complex.

## Slide 8: Conﬁguration Space Header
Each device has a conﬁguration space header.
can be up to 256 bytes
A device can optionally have an extended capabilities register at offsets in range 256 to 4095

## Slide 9: Mechanisms to generate Configuration Space Transactions
. Processors cannot natively generate a PCI conﬁguration cycle; the PCI conﬁguration space transactions can be generated by either of the following mechanisms (on Intel architecture systems):
1. Indirect mode:
A) Use a sequence of I/O transaction to write to address port at I/O address 0xCF8 followed by read/write to Data Port register at I/O address 0xCFC.
B) The address register is written with the PCI conﬁguration address to read, and then content is read/written to by accessing the data port register.
C) This mechanism allows accessing of ﬁrst 256 conﬁguration registers; extended capability registers in range [256–4095] can be assessed only through the MMIO mechanism described next.

## Slide 10
MMIO: Up to 256-MB (max 4K per device * 65,536 devices) conﬁguration space is mapped into the processor’s memory-mapped address space.
Reads or writes to this address space generate the conﬁguration transactions on the PCI bus.
The MMIO address bits are built up from the following bit ﬁelds:
A[32:28] = MMIO conﬁguration space: base of which is set by the MMBAR register
A[27:20] =PCI bus number
A[19:15] = Device number on bus
A[14:12] = Device function number (up to 8) •
A[11:8] =Extended register
A[7:2] =Register number
A[1:0] = Byte select for a register

## Slide 11: Base Configuration Header
allows the system software to identify the device type and to assign memory and interrupts to the device.
The vendor ID identiﬁes the manufacturer of the function
IDs are assigned by the PCI-SIG.
used by operating systems to ﬁnd the appropriate device driver to load and associate with the device
The device revision can be used to adapt the driver for speciﬁc versions of the device.
Class code: provide a generic device driver support for a device.
the device ID is ignored and the operating system assigns the device driver based on class code
Example : VGA adapter

## Slide 12: Register Spaces- configuration space
composed of two different register spaces, the conﬁguration space and device registers
conﬁguration space is primarily used as part of the enumeration and allocating the driver to the device.
The conﬁguration space contains a number of base address registers.
These base address registers are programmable decoders that are used to decode access to the actual device registers

## Slide 13: Base Address Registers
There are six 32-bit or three 64-bit base address register
contains some read-only low-order bits set to zero
When you write all ones to the base address register and read back the value, the enumeration software establishes the size of memory the enumeration software must allocate.
lower byte of the base address register indicates whether the base address is to allocate memory or I/O space
. It also includes an prefetchability attribute
Indicates if the memory is prefetchable
Base address register is written, all memory transactions generated to that bus address range are claimed by the device.
addresses are assigned to be in noncacheable memory-mapped I/ O space by the busenumeration software at startup

## Slide 14: Bus Addresses
addresses used on the bus
Intel- platforms -there is a one-to-one correspondence between the host physical address and the address used on the bus

## Slide 15
The interrupts vectors are also assigned during the enumeration process.
Each PCIe device provides conﬁguration registers to support a feature known as MSI/MSI-X.
There are two key register types: the ﬁrst is an address register and the second is a data register.
The address is a special address in the system, and it is the targeted interrupt controller for which the interrupt is being sent to. Each processor hardware thread has an individual target address, so MSI/MSI-X interrupts can be steered to a speciﬁc hardware processor thread
.

## Slide 16
The data register is the vector for the interrupt that is assigned to the device.
The device can request multiple interrupt vectors, and the enumeration process attempts to satisfy all device requests with individual interrupt vectors.
In cases where there is oversubscription of inter- rupt vectors versus device requirements, (i.e. the system cannot allocate all the vectors requested by the device), some vectors must be shared among different functions within a device. Having many separate vectors for a device can improve the performance of an interrupt handling routing, as it does not have to read device status registers to ﬁnd out the cause of the interrupt