## Slide 1: Device Interconnect
Low Performance

## Slide 2: Device Interconnect
Inter Integrated Circuit Bus
System Management Bus
Serial Peripheral Interface Bus
Inter IC Sound
Universal Asynchronous Receiver/Transmitter(UART)
High-Speed Serial

## Slide 3: Inter-Integrated Circuit Bus
One of the most prevalent buses is Inter-Integrated Bus (or) I2C invented by Philips (now NXP) in 1980s.
The bus standard allows for multiple masters( however, in many cases it runs as a single master with multiple slaves) on the bus.
It consists of 2 bi-directional wires namely,
A Serial Clock Line (SCL)
A Serial Data Line (SDL)
Each Device consists of an Open Collector to bring the pin down to zero.

## Slide 4: Inter-Integrated Circuit Bus

## Slide 5: Inter-Integrated Circuit Bus
The master device generates the serial clock, controls bus access, and controls the stop and start conditions.
The clock speeds are relatively low, from 10 kHz to 100 kHz and 400 kHz to 2 MHz .
Each device has a 7-bit address.
Low 3 bits for Device Selection.
High 4 bits for Device Type Selection.

## Slide 6: Inter-Integrated Circuit Bus
To Start--> SDA  High to Low;
SCL  High;
SDA can when SCL is low.
When the SCL is low, the next bit of data is clocked into SDA.
This is repeated for each bit in turn starting with the MSB.
To Stop--> SDA  Low to High;
SCL  High;
Bus Not Busy – When both SDA and SCL are high

## Slide 7: Inter-Integrated Circuit Bus
To perform a byte write to the device, the two bytes following in the device address specify an address to write within the device, and the following byte is the byte we wish to write to the address within the device.
Read in the device can take two forms;
the first is a current address read capability. The device has an address counter that starts at zero. Each read of the device provides a byte back to the master and the counter is incremented.
There is also an address specific read, but this is accessed by setting the counter using a device write sequence, then reading back the current address value.

## Slide 8: System Management Bus
The System Management Bus is a two-wire bus used for host-to-device and device-to-device communications.
SMBus permits a bus speed for an SMBus of between 10 KHz and 100 KHz.
SMBus has also defined a mechanism for a slave to send a notification to the host (not unlike an I2C slave device becoming the master for a particular transaction).

## Slide 9: System Management Bus
The SMBus specification defines a number of commands for use with devices:
Quick Command – This is the simplest message that can be sent to a device; the only data communicated is the address byte where the read/write bit is only data indication. It can be used to simply turn the device on or off.
Send Byte – A simple device will recognize its slave address and process the subsequent data byte as a command.
Receive Byte – Similar to send byte, but gets a data byte from the device. When the device is read it provides a single byte.
Write Byte/Word – The first byte of a Write Byte/Word sequence is the command code. The next one or two bytes are the data to be written to the device.

## Slide 10: System Management Bus
Read Byte/Word – To read a byte from the device, the host must first write a command to the slave device. Then the host must follow that with repeated START commands to denote a read from the slave; the slave returns one or two bytes of data.
Process Call – This sends data to the slave device and waits for a response byte based on the data sent to the device.
Block Read/Write – This is an extension of the read/write byte where a number of bytes to be sent or received is added is indicated after the command byte.
Block Write-Block Read Process Call – This is an combination of block write and process call: it allows for the transmission of multiple bytes as the “argument” to the process call. The response can also be a variable number of bytes.

## Slide 11: System Peripheral Interface
Serial Peripheral Interface (SPI) is a four-wire bus.
It consists of a serial clock, master output/slave input, master input/slave output, and a device select pin.
Speeds up to 80 MHz
These additional data bits dramatically increase the performance.
The SPI bus is used to connect to serial flash parts that provide the initial boot code for Intel platforms

## Slide 12: System Peripheral Interface

## Slide 13: Inter IC Sound (I2S)
The I2S bus is another bus defined by Philips.
The bus was designed to transfer audio samples between integrated circuits.
The bus is a three-wire bus: a continuously running clock, a data line, and a word select line to allow for the selection of two channels (left/right for stereo), which are time-multiplexed on the data pins.