## Slide 2: Platform Overview…
Processor
  Modern embedded SOC (32 bit processor)
    Application processor
    Baseband processor
  RISC vs CISC
  Scalar and Super scalar
System memory map
  Memory space vs I/O space
  System Map
    System DRAM
    MMIO
      Fixed address
      PCIe bus

## Slide 3: Platform Overview…
Interrupt Controller
  real time service
  3 registers: status, mask and pending
  Interrupt priority and s/w algorithm
  Interrupt vector table
    S/w implemented & hardware generated
  Interrupt lines
    Level/edge triggered
  Intel architecture specific
    PIC (8259) & APIC
  8259
    8 interrupt lines & 15 lines using master slave cascading
    Registers: Interrupt request register, Interrupt in-service, Interrupt mask register
    Poor support to multicore, latency etc.,

## Slide 4: Platform Overview…
  APIC
    Introduced with Pentium, PIC should be disabled
    2 components: Local APIC & I/O APIC
    2 primary functions of local APIC
      Receive interrupts normally & send it to processor
      Inter processor interrupt messages in multiple processor system
    Local APIC registers controls IPI messages & local interrupts
    I/O APIC
      Receive external interrupts & send to local APIC
  Sources for Local APIC
    Locally connected I/O devices
    Externally connected I/O devices
    IPI
    APIC timer generated interrupts
    Thermal sensor interrupts
    APIC internal error interrupt
    Local vector table for local APIC

## Slide 5: Platform Overview…
  I/O APIC on SOC
    24 individual interrupt sources
    I/O APIC interrupt source and its generated vector is in I/O APIC interrupt redirection table (10H to FEH)
    3 registers
      Index
      Window
      EOI register
    RIRR: Remote interrupt request register should be cleared

## Slide 6: Platform Overview…
Timers
  H/W counters & called as OS tick
  Attributes of timer
    Clock source, timer accuracy, free run/oneshot, count direction, counters and watch dog timers
  Intel timers/counters
    8253/4 legacy PIT timer block
    High precision event timers
    Local APIC interrupt timer
    Watchdog timer
    3 counters: counter0, counter1, counter2
    Working of counter(8253): setting control word bits and load count value
  Local APIC timer
    4 registers: divide configuration, initial count, current count, local vector table
  Watchdog
    Range: 1 microseconds to 10 minutes
    35 bit down counter in Atom processor
    First stage: Interrupt
    Second stage: Assert GPIO pin/ Warm reset / Cold reset

## Slide 7: Device Interface
Device interface: consists of controller and external interconnect
Peripheral bus interface capabilities
  Transaction mapping from processor to device address space
  Inbound transactions
  Interrupts
  Physical standard
Range of bus definitions from well defined PCI to local standards

## Slide 8: Peripheral Component Interconnect
High performance
Third generation : PCI Express (PCIe)
Bus Enumeration: Identification of device & dynamic resource allocation.
Configuration space: 256MB
Three tuple address called Bus Device Function
  PCIe busses (upto 256)
  Devices per bus (upto 32)
  Functions per device (upto 8)
Each device configuration header: 256 bytes with extended register offset range 256 to 4095
65536 devices are supported theoretically

## Slide 9: Peripheral Component Interconnect…
Addressing mode:
  Indirect mode : same as default
  MMIO : extended usage (address array details refer book)
Configuration Header (CH):
  Vendor id: manufacturers
  Class code : generic (no device id)
  Device registers accessed by decoding base address register in CH
Interrupt vectors

## Slide 10: Peripheral Component Interconnect…
Bus mastering
  Device ability to read/write host memory
  Circular buffer
  Bus to physical address conversion routine needed
Transaction ordering

## Slide 11: Universal Serial Bus (USB)
Low voltage differential pair serial bus
Hot pluggable
Special sequence at commencement for clock
Micro USB connector: 100mA to 500mA Eg. cell phones, touch screens etc.
Different speeds:
  Low: 1.5Mbps (USB 1.0/1.1)
  Full: 12 Mbps (USB 1.0/1.1/2.0)
  High: 480 Mbps (USB 2.0)
Support compatibility
2 sides – host side and device side (host may act as device in other case with USB On The Go)
127 devices supported by simple hub device

## Slide 12: Universal Serial Bus…
Bus Protocol: built in error handling, fault recovery
Bus enumeration starts when device connected
Host-Device communication: Token ( direction, type ,endpoint address), Data, Handshake
Exchange Data/Control through logical pipe
Data transfers (4)
  Control, bulk data, Interrupt data, Isochronous data
  Cannot mixed in single pipe
Control pipe: set_address, set_configuration, get_descriptor
4 standard information: Vendor id, device class, power mgmt. capabilities, endpoint description
Command: lsusb –v (shows: device, configuration, interface, endpoint descriptor)
Interface standards supported: bluetooth, smartcard interface, hub, mass storage, modem, video, USB audio etc.,
Bandwidth: 1ms frames with 125µs micro frames
Linked list of transfer descriptor called frame list.

## Slide 13: USB Programming interface
UHCI (Universal Host Controller Interface)
  USB 1.x
OHCI (Open HCI)
  USB 1.x
EHCI (Extended HCI)
  USB 2.0
USBOTG
  No std. host controller interface

## Slide 14: USB Programming interface…
PCI-EHCI Controller
  2 key list : Periodic (high priority) Asysnchronous
  Asynchronous list address, head queues & payload description
  Linux driver: core & set of classes for read/ write/ format the payload

## Slide 15: Device Interconnect
Low speed
Low pin count
Low performance interface
Various kinds are:
  Inter-integrated Circuit Bus
  System Mgmt Bus
  Serial Peripheral Interface Bus
  Inter IC Sound
  Universal Asynchronous Receiver/Transmitter
  High Speed Serial

## Slide 16: Inter-Integrated Circuit Bus
Multiple masters
Serial clock (SC) and serial data(SD) : each is bidirectional
Open collector gates are used to drive the devices
7bit addresses, A0 to A2: device, A3 to A6: device type (112 devices are supported, rest are for control)
Master controls the bus transfers
  Bus not busy, start bus transfer, transfer data(SCL &SDL), Acknowledgement after every byte, stop bus transfer.

## Slide 17: System Management Bus
2 wire bus
PC motherboards – power supply, sensors, fan control.
Integrates devices & SMBus host controller
Speed 10khz and 100khz
Commands: Quick command, send/receive byte, write/read byte/word, process call, Block read/write, block writeback read process call

## Slide 18: Serial Peripheral interface
4 wire bus: serial clock, master o/p or slave i/p, master i/p or slave o/p, device select pin.
Speed is higher than I2C, SMBus
No standard specification
Used to connect serial flash ports
Audio Buses
More pin count is needed
Codec to a digital SOC
High defn. audio bus: 16 channels/stream
DMA engines available

## Slide 19: Inter IC Sound
Philips - 3 wire bus: continuous clock, data line, word select line
Audio samples between ICs
Universal Asynchronous Receiver Transmitter
Peer UART to transmit & receive
EIA stds: RS-232, RS-422 & RS-485
3 wires: transmit, receive and eletrical ground
Null modem cable
Simple command console and boot indication
Use MAX232 as level shifter if UART is not compatible with RS-232

## Slide 20: Universal Asynchronous Receiver Transmitter…
Asynchronous – stop and start bits
Different speeds: 300,600,1200,1800,2400,4800,7200,9600…..
Flow control:
  H/w : RTS and CTS
  S/w: Special code for start, pause etc..,
Binary format – kermit: terminal emulation program
Linux serial driver configure 8250 & 16550A
UART with DMA eg: Bluetooth usage model
Notes: 9600 is the most common speed

## Slide 21: Intel Atom E6XX series platforms
The capabilities of E6XX series devices
  One atom core: 600Mhz, 1, 1.3, 1.6GHz
  2 wide instruction decode and in order execution
  32 kB 4-way level 1 instruction cache
  24 kB 6-way level 1 data cache
  512 kB 8-way level 2 cache
  2 h/w threads
  Primary expansion via PCIe etc.,
  Internal coherence
  Graphics controller
  H/W video decoder & encoder
  High definition audio interface
  SMBus,SPI, 14 GPIO, JTAG, PCI

## Slide 22: Intel Atom E6XX series platforms…
Platform Controller Hub (PCH) – ability to extend the platform
PCI
USB host
USB device
GbE MAC–Gb Ethernet MAC
SATA
SDHC
IEEE 1588 block
SPI
CAN
I2C
UART
GPIO – 12 bit
JTAG – boundary scan
Serial ROM I/F
OKI Semiconductor
ST microelectronics
Discrete device expansion
FPGA Expansion
Eg: EG20T Platform Controller Hub Refer book for figure